## Slide 1: Electric Fan
CONSUMER ELECTRONICS

## Slide 2: External Parts

## Slide 3: Fleming’s Left Hand Rule
Force
Current
Magnetic Field
Current

## Slide 4: Objectives
The students can identify the internal parts of an electric fan.
The students can able to perform troubleshooting in the electric fan in setting the rotor’s speed.

## Slide 5: What is Electric fan?
It is a type of electronic appliances that is run by an electronic motor.

## Slide 6: Purpose Of The Electric
Fan
To convert electrical energy to mechanical energy.
Electrical
Energy
Mechanical Energy

## Slide 7
To make consumers feel comfortable during hot seasons or summer days.

## Slide 8: Internal Parts Of The Electric Fan

## Slide 9: Selector Switch
It is a part of electric fan that can intensify the produce air for the consumers.
Rotary Switch
Push Button Switch

## Slide 10: Electric Motor
It is the main part of the electric fan that produces mechanical energy to make the propeller rotate.

## Slide 11: Rotor
It is the movable part of the electrical motor that rotates

## Slide 12: Stator
It is a non movable part of the electric motor that provides electro magnetic energy to the rotor.

## Slide 13: Copper Winding
It is a set of copper wire that
supplies electricity in the stator and rotor.
Copper Winding in Rotor
Copper Winding in
Stator

## Slide 14
Setting the speed of the electric fan requires:
Electric Motor
Selector Switch
Handtools
Terminal Block

## Slide 15: Current and Resistance
The Higher Resistance means a Low Current which will result slow rotation of the propeller.

## Slide 16
The Lower Resistance means a Higher Current which will result in fast rotation of the propeller.

## Slide 17: Fan Speed Control

## Slide 18
Since that the no.1 in the selector switch has a slow rotation of rotor it means that the resistance needed is high.

## Slide 19
No.2 in the selector switch will have a moderate resistance and the no.3 has a lowest resistance

## Slide 20
1
2
3
0

## Slide 21
3
2
1
0

## Slide 22: Terminal Block
ohms 320
ohms 330
ohms
Common
3
2
1
Common
Line
Cord
Motor
Selector Switch
Example resistance
300

## Slide 23: Fan Regulator

## Slide 24
 Fan Regulators have an important place in the electrical switch boards.
 Fan Regulators are very similar to light dimmers . Their function is regulate/control the speed of the fan and provide a convenient environment environment for the residents.
 The traditional regulators which are bulky use a resistance having taps and connected in series with the fan.when we move the knob different amount of resistance gets inserted in the circuit

## Slide 26: Let’s Have a Quiz

## Slide 27: Identification

## Slide 28
1)
It is a movable part of the motor which rotates.

## Slide 29: 2)
It is a non movable part of the electric motor that provides electro magnetic energy to the rotor.

## Slide 30: 3)
It is a part of electric fan that can intensify the produce air for the consumers.

## Slide 31: Picture Identification

## Slide 32
4)

## Slide 33
5)

## Slide 34: Identification

## Slide 35: 1) Rotor
It is a movable part of the motor which rotates.

## Slide 36: 2) Stator
It is a non movable part of the electric motor that provides electro magnetic energy to the rotor.

## Slide 37: 3) Selector Switch
It is a part of electric fan that can intensify the produce air for the consumers.

## Slide 38: Picture Identification

## Slide 39: 4) Electric Motor

## Slide 40: 5) Copper Winding

## Slide 41
Schematic Diagram of an Electric Fan

## Slide 42: Assignment
Research about the different models or types of electric fan and it’s uses.
Write your assignments in your notebook.

## Slide 43: Good Bye Class