## Slide 2
WHAT IS RESISTOR ?
TYPES OF RESISTOR.
CONNECTION OF RESISTOR.
RESISTOR COLOUR CODE
RESISTOR POWER RATING

## Slide 3
A RESISTOR IS A PASSIVE TWO - TERMINAL ELECTRICAL COMPONENT THAT IMPLEMENTS ELECTRICAL RESISTANCE AS A CIRCUIT ELEMENT.
THE RATIO OF THE VOLTAGE APPLIED ACROSS A RESISTOR'S TERMINALS TO THE INTENSITY OF CURRENT THROUGH THE CIRCUIT IS CALLED RESISTANCE.
THIS RELATION IS REPRESENTED BY OHM'S
LAW:
V = I R

## Slide 4: UNIT SYMBOL
THE OHM (SYMBOL: Ω) IS THE SI UNIT
OF ELECTRICAL RESISTANCE, NAMED AFTER GEORG SIMON OHM.
AN OHM IS EQUIVALENT TO A VOLT PER AMPERE
OTHER DERIVED UNITS ARE MILLI OHM (1 MΩ =
10−3 Ω), KILO OHM (1 KΩ = 103 Ω), AND MEGA OHM (1 MΩ
= 106 Ω).
FIXED RESISTOR
VARIABLE RESISTOR

## Slide 5: TYPES OF RESISTOR

## Slide 6: TYPES OF RESISTOR
RESISTOR
FIXED RESISTOR
VARIABLE RESISTOR

## Slide 7: VARIABLE RESISTOR
FIXED RESISTOR
CARBON COMPOSITE RESISTOR
FILM RESISTOR
WIRE WOUND RESISTOR
RESISTANCE WIRE
RHEOSTAT
POTENTIOMETER
THERMISTOR
HUMISTOR
VARISTOR
PHOTORESISTOR

## Slide 8: CARBON COMPOSITE RESISTOR
LOW INDUCTANCE
IDEAL FOR HIGH FREQUENCY APPLICATIONS
VERY CHEAP TO MAKE
HAVE VERY LARGE TOLERANCES

## Slide 9: FILM RESISTOR
THE RESISTIVE VALUE OF THE RESISTOR IS CONTROLLED BY INCREASING THE DESIRED THICKNESS OF THE DEPOSITED FILM.
RESISTANE UPTO 10MΩ CAN BE OBTAINED.
HAVE TOLERANCE 1% OR LESS

## Slide 10: WIRE WOUND RESISTOR
MADE BY WINDING A THIN METAL ALLOY WIRE ONTO AN INSULATING CERAMIC FORMER IN THE FORM OF A SPIRAL HELIX
AVAILABLE IN VERY LOW OHMIC AND HIGH PRECISION VALUES
(FROM 0.01 TO 100KΩ)

## Slide 11: RHEOSTAT
RHEOSTAT IS A ADJUSTABLE RESISTOR USED IN APPLICATIONS THAT REQUIRE ADJUSTMENT OF CURRENT OR VARYING OF RESISTANCE IN
AN ELECTRIC CIRCUIT
A SPECIAL TYPE OF RHEOSTAT IS THE POTENTIOMETER

## Slide 12: POTENTIOMETER
A POTENTIOMETER IS, A POT, IN ELECTRONICS TECHNOLOGY IS A THREE-TERMINAL RESISTOR WITH A SLIDING CONTACT THAT FORMS AN ADJUSTABLE VOLTAGE DIVIDER.
POTENTIOMETERS ARE COMMONLY USED TO CONTROL ELECTRICAL DEVICES SUCH AS VOLUME CONTROLS, JOYSTICKS ETC.

## Slide 13: THERMISTOR
A THERMISTOR IS A TYPE
OF RESISTOR WHOSE RESISTANCE VARIES SIGNIFICANTLY
WITH TEMPERATURE
THERMISTORS CAN BE USED AS CURRENT-LIMITING DEVICES FOR CIRCUIT PROTECTION, AS REPLACEMENTS FOR FUSES

## Slide 14: HUMISTOR
A HUMISTOR IS A TYPE
OF RESISTOR WHOSE RESISTANCE VARIES SIGNIFICANTLY
WITH HUMIDITY
A HUMIDITY SENSOR MEASURES THE HUMIDITY LEVEL BY MEASURING THE CHANGE IN
THE RESISTANCE OF AN ELEMENT

## Slide 15: VARISTOR
A VARISTOR (OR VOLTAGE DEPENDENT RESISTOR ) FUNCTION IS TO CONDUCT SIGNIFICANTLY INCREASED CURRENT WHEN VOLTAGE IS EXCESSIVE.
HIGH VOLTAGE VARISTOR

## Slide 16: PHOTORESISTOR
A PHOTORESISTOR OR LIGHT DEPENDENT RESISTOR (LDR) EXHIBITS PHOTOCONDUCTIVITY.
PHOTORESISTORS IN MANY CONSUMER ITEMS SUCH AS STREET LIGHTS, CLOCK RADIOS, ALARM DEVICES ETC

## Slide 17: CONNECTION OF RESISTORS

## Slide 18: SERIES CONNECTION
IN SERIES CONNECTION, THE CURRENT REMAINS CONSTANT.
(i.e. I = I1 = I2 = …. = In )
IN SERIES CONNECTION, VOLTAGE ADDS UP. (i.e. V = V1 + V2 + …. + Vn)

## Slide 19: PARALLEL CONNECTION
IN PARALLEL CONNECTION, THE VOLTAGE REMAINS CONSTANT.
(i.e. V = V1 = V2 = …. = Vn)
IN PARALLEL CONNECTION, CURRENT ADDS UP.
(i.e. I = I1 + I2 + …. + In )

## Slide 20: RESISTOR COLOUR CODE

## Slide 21: RESISTOR VALUE = XY * Z ± TOLERANCE
EXAMPLE:-
FIND THE RESISTANCE OF THE GIVEN RESISTOR ?

## Slide 22: COLOUR CODE TABLE
COLOUR | DIGIT | MULTIPLIER | TOLERANCE
BLACK | 0 | 100 | -
BROWN | 1 | 101 | ± 1%
RED | 2 | 102 | ± 2%
ORANGE | 3 | 103 | -
YELLOW | 4 | 104 | -
GREEN | 5 | 105 | ± 0.5%
BLUE | 6 | 106 | ± 0.25%
VIOLET | 7 | 107 | ± 0.1%
GREY | 8 | 108 | -
WHITE | 9 | 109 | -
GOLD | - | 10-1 | ± 5%
SILVER | - | 10-2 | ± 10%
NONE | - | - | ± 15%

## Slide 23: POWER RATING

## Slide 24: RESISTOR POWER RATING
THE POWER RATING OF RESISTORS CAN BE CALCULATED USING THE FORMULA :-
THE LARGER THE POWER RATING, THE GREATER THE PHYSICAL SIZE OF THE RESISTOR.
WHEN USED IN AC CIRCUITS THE AC IMPEDANCE OF A RESISTOR IS EQUAL TO ITS DC RESISTANCE.

## Slide 25: CITATION
www.google.com
en.wikipedia.org
www.electronics-tutorials.ws